## Slide 1: What is the effect of excessive microphone gain on SSB transmissions?
Frequency instability
Distorted transmitted audio
Increased SWR
All these choices are correct
T4B01 HRLM (5 - 8)

## Slide 2: What is the effect of excessive microphone gain on SSB transmissions?
Frequency instability
Distorted transmitted audio
Increased SWR
All these choices are correct
(B) T4B01 HRLM (5 - 8)

## Slide 3: Which of the following can be used to enter a transceiver’s operating frequency?
A. The keypad or VFO knob
B. The CTCSS or DTMF encoder
C. The Automatic Frequency Control
D. All of these choices are correct
T4B02 HRLM (5 - 5)

## Slide 4: Which of the following can be used to enter a transceiver’s operating frequency?
A. The keypad or VFO knob
B. The CTCSS or DTMF encoder
C. The Automatic Frequency Control
D. All of these choices are correct
(A) T4B02 HRLM (5 - 5)

## Slide 5: How is squelch adjusted so that a weak FM signal can be heard?
Set the squelch threshold so that receiver output audio is on all the time
Turn up the audio level until it overcomes the squelch threshold
Turn on the anti-squelch function
Enable squelch enhancement
T4B03 HRLM (5 - 8)

## Slide 6: How is squelch adjusted so that a weak FM signal can be heard?
Set the squelch threshold so that receiver output audio is on all the time
Turn up the audio level until it overcomes the squelch threshold
Turn on the anti-squelch function
Enable squelch enhancement
(A) T4B03 HRLM (5 - 8)

## Slide 7: What is a way to enable quick access to a favorite frequency or channel on your transceiver?
Enable the frequency offset
Store it in a memory channel
Enable the VOX
Use the scan mode to select the desired frequency
T4B04 HRLM (5 - 5)

## Slide 8: What is a way to enable quick access to a favorite frequency or channel on your transceiver?
Enable the frequency offset
Store it in a memory channel
Enable the VOX
Use the scan mode to select the desired frequency
(B) T4B04 HRLM (5 - 5)

## Slide 9: What does the scanning function of an FM transceiver do?
Checks incoming signal deviation
Prevents interference to nearby repeaters
Tunes through a range of frequencies to check for activity
Checks for messages left on a digital bulletin board
T4B05 HRLM (6 - 10)

## Slide 10: What does the scanning function of an FM transceiver do?
Checks incoming signal deviation
Prevents interference to nearby repeaters
Tunes through a range of frequencies to check for activity
Checks for messages left on a digital bulletin board
(C) T4B05 HRLM (6 - 10)

## Slide 11: Which of the following controls could be used if the voice pitch of a single-sideband signal returning to your CQ call seems too high or low?
A. The AGC or limiter
B. The bandwidth selection
C. The tone squelch
D. The receiver RIT or clarifier
T4B06 HRLM (5 - 9)

## Slide 12: Which of the following controls could be used if the voice pitch of a single-sideband signal returning to your CQ call seems too high or low?
A. The AGC or limiter
B. The bandwidth selection
C. The tone squelch
D. The receiver RIT or clarifier
(D) T4B06 HRLM (5 - 9)

## Slide 13: What does a DMR “code plug” contain?
Your call sign in CW for automatic identification
Access information for repeaters and talkgroups
The codec for digitizing audio
The DMR software version
T4B07 HRLM (6 - 13)

## Slide 14: What does a DMR “code plug” contain?
Your call sign in CW for automatic identification
Access information for repeaters and talkgroups
The codec for digitizing audio
The DMR software version
(B) T4B07 HRLM (6 - 13)

## Slide 15: What is the advantage of having multiple receive bandwidth choices on a multimode transceiver?
A. Permits monitoring several modes at once by selecting a separate filter for each mode
B. Permits noise or interference reduction by selecting a bandwidth matching the mode
C. Increases the number of frequencies that can be stored in memory
D. Increases the amount of offset between receive and transmit frequencies
T4B08 HRLM (5 - 9)

## Slide 16: What is the advantage of having multiple receive bandwidth choices on a multimode transceiver?
A. Permits monitoring several modes at once by selecting a separate filter for each mode
B. Permits noise or interference reduction by selecting a bandwidth matching the mode
C. Increases the number of frequencies that can be stored in memory
D. Increases the amount of offset between receive and transmit frequencies
(B) T4B08 HRLM (5 - 9)

## Slide 17: How is a specific group of stations selected on a digital voice transceiver?
By retrieving the frequencies from transceiver memory
By enabling the group’s CTCSS tone
By entering the group’s identification code
By activating automatic identification
T4B09 HRLM (6 - 13)

## Slide 18: How is a specific group of stations selected on a digital voice transceiver?
By retrieving the frequencies from transceiver memory
By enabling the group’s CTCSS tone
By entering the group’s identification code
By activating automatic identification
(C) T4B09 HRLM (6 - 13)

## Slide 19: Which of the following receiver filter bandwidths provides the best signal-to-noise ratio for SSB reception?
A. 500 Hz
B. 1000 Hz
C. 2400 Hz
D. 5000 Hz
T4B10 HRLM (5 - 9)

## Slide 20: Which of the following receiver filter bandwidths provides the best signal-to-noise ratio for SSB reception?
A. 500 Hz
B. 1000 Hz
C. 2400 Hz
D. 5000 Hz
(C) T4B10 HRLM (5 - 9)

## Slide 21: Which of the following must be programmed into a D-STAR digital transceiver before transmitting?
Your call sign
Your output power
The codec type being used
All these choices are correct
T4B11 HRLM (6 - 13)

## Slide 22: Which of the following must be programmed into a D-STAR digital transceiver before transmitting?
Your call sign
Your output power
The codec type being used
All these choices are correct
(A) T4B11 HRLM (6 - 13)

## Slide 23: What is the result of tuning an FM receiver above or below a signal’s frequency?
Change in audio pitch
Sideband inversion
Generation of a heterodyne tone
Distortion of the signal’s audio
T4B12 HRLM (5 - 9)

## Slide 24: What is the result of tuning an FM receiver above or below a signal’s frequency?
Change in audio pitch
Sideband inversion
Generation of a heterodyne tone
Distortion of the signal’s audio
(B) T4B12 HRLM (5 - 9)