## Slide 1: What type of radiation are VHF and UHF radio signals?
A. Gamma radiation
B. Ionizing radiation
C. Alpha radiation
D. Non-ionizing radiation
T0C01 HRLM (9 - 11)

## Slide 2: What type of radiation are VHF and UHF radio signals?
A. Gamma radiation
B. Ionizing radiation
C. Alpha radiation
D. Non-ionizing radiation
(D) T0C01 HRLM (9 - 11)

## Slide 3: At which of the following frequencies does maximum permissible exposure have the lowest value?
A. 3.5 MHz
B. 50 MHz
C. 440 MHz
D. 1296 MHz
T0C02 HRLM (9 - 12)

## Slide 4: At which of the following frequencies does maximum permissible exposure have the lowest value?
A. 3.5 MHz
B. 50 MHz
C. 440 MHz
D. 1296 MHz
(B) T0C02 HRLM (9 - 12)

## Slide 5: How does the allowable power density for RF safety change if duty cycle changes from 100 percent to 50 percent?
It increases by a factor of 3
It decreases by 50 percent
It increases by a factor of 2
There is no adjustment allowed for lower duty cycle
T0C03 HRLM (9 - 13)

## Slide 6: How does the allowable power density for RF safety change if duty cycle changes from 100 percent to 50 percent?
It increases by a factor of 3
It decreases by 50 percent
It increases by a factor of 2
There is no adjustment allowed for lower duty cycle
(C) T0C03 HRLM (9 - 13)

## Slide 7: What factors affect the RF exposure of people near an amateur station antenna?
A. Frequency and power level of the RF field
B. Distance from the antenna to a person
C. Radiation pattern of the antenna
D. All of these choices are correct
T0C04 HRLM (9 - 14)

## Slide 8: What factors affect the RF exposure of people near an amateur station antenna?
A. Frequency and power level of the RF field
B. Distance from the antenna to a person
C. Radiation pattern of the antenna
D. All of these choices are correct
(D) T0C04 HRLM (9 - 14)

## Slide 9: Why do exposure limits vary with frequency?
A. Lower frequency RF fields have more energy than higher frequency fields
B. Lower frequency RF fields do not penetrate the human body
C. Higher frequency RF fields are transient in nature
D. The human body absorbs more RF energy at some frequencies than at others
T0C05 HRLM (9 - 11)

## Slide 10: Why do exposure limits vary with frequency?
A. Lower frequency RF fields have more energy than higher frequency fields
B. Lower frequency RF fields do not penetrate the human body
C. Higher frequency RF fields are transient in nature
D. The human body absorbs more RF energy at some frequencies than at others
(D) T0C05 HRLM (9 - 11)

## Slide 11: Which of the following is an acceptable method to determine that your station complies with FCC RF exposure regulations?
A. By calculation based on FCC OET Bulletin 65
B. By calculation based on computer modeling
C. By measurement of field strength using calibrated equipment
D. All of these choices are correct
T0C06 HRLM (9 - 14)

## Slide 12: Which of the following is an acceptable method to determine that your station complies with FCC RF exposure regulations?
A. By calculation based on FCC OET Bulletin 65
B. By calculation based on computer modeling
C. By measurement of field strength using calibrated equipment
D. All of these choices are correct
(D) T0C06 HRLM (9 - 14)

## Slide 13: What hazard is created by touching an antenna during a transmission?
Electrocution
RF burn to skin
Radiation poisoning
D. All of these choices are correct
T0C07 HRLM (9 - 11)

## Slide 14: What hazard is created by touching an antenna during a transmission?
Electrocution
RF burn to skin
Radiation poisoning
All of these choices are correct
(B) T0C07 HRLM (9 - 11)

## Slide 15: Which of the following actions can reduce exposure to RF radiation?
A. Relocate antennas
B. Relocate the transmitter
C. Increase the duty cycle
D. All of these choices are correct
T0C08 HRLM (9 - 14)

## Slide 16: Which of the following actions can reduce exposure to RF radiation?
A. Relocate antennas
B. Relocate the transmitter
C. Increase the duty cycle
D. All of these choices are correct
(A) T0C08 HRLM (9 - 14)

## Slide 17: How can you make sure your station stays in compliance with RF safety regulations?
A. By informing the FCC of any changes made in your station
B. By re-evaluating the station whenever an item of equipment is changed
C. By making sure your antennas have low SWR
D. All of these choices are correct
T0C09 HRLM (9 - 14)

## Slide 18: How can you make sure your station stays in compliance with RF safety regulations?
A. By informing the FCC of any changes made in your station
B. By re-evaluating the station whenever an item of equipment is changed
C. By making sure your antennas have low SWR
D. All of these choices are correct
(B) T0C09 HRLM (9 - 14)

## Slide 19: Why is duty cycle one of the factors used to determine safe RF radiation exposure levels?
It affects the average exposure to radiation
It affects the peak exposure to radiation
It takes into account the antenna feed line loss
It takes into account the thermal effects of the final amplifier
T0C10 HRLM (9 - 13)

## Slide 20: Why is duty cycle one of the factors used to determine safe RF radiation exposure levels?
It affects the average exposure to radiation
It affects the peak exposure to radiation
It takes into account the antenna feed line loss
It takes into account the thermal effects of the final amplifier
(A) T0C10 HRLM (9 - 13)

## Slide 21: What is the definition of duty cycle during the averaging time for RF exposure?
A. The difference between the lowest power output and the highest power output of a transmitter
B. The difference between the PEP and average power output of a transmitter
C. The percentage of time that a transmitter is transmitting
D. The percentage of time that a transmitter is not transmitting
T0C11 HRLM (9 - 13)

## Slide 22: What is the definition of duty cycle during the averaging time for RF exposure?
A. The difference between the lowest power output and the highest power output of a transmitter
B. The difference between the PEP and average power output of a transmitter
C. The percentage of time that a transmitter is transmitting
D. The percentage of time that a transmitter is not transmitting
(C) T0C11 HRLM (9 - 13)

## Slide 23: How does RF radiation differ from ionizing radiation (radioactivity)?
RF radiation does not have sufficient energy to cause chemical changes in cells and damage DNA
RF radiation can only be detected with an RF dosimeter
RF radiation is limited in range to a few feet
RF radiation is perfectly safe
T0C12 HRLM (9 - 11)

## Slide 24: How does RF radiation differ from ionizing radiation (radioactivity)?
RF radiation does not have sufficient energy to cause chemical changes in cells and damage DNA
RF radiation can only be detected with an RF dosimeter
RF radiation is limited in range to a few feet
RF radiation is perfectly safe
(A) T0C12 HRLM (9 - 11)

## Slide 25: Who is responsible for ensuring that no person is exposed to RF energy above the FCC exposure limits?
The FCC
The station licensee
Anyone who is near an antenna
The local zoning board
T0C13 HRLM (9 - 11)

## Slide 26: Who is responsible for ensuring that no person is exposed to RF energy above the FCC exposure limits?
The FCC
The station licensee
Anyone who is near an antenna
The local zoning board
(B) T0C13 HRLM (9 - 11)