## Slide 1: Which of the following is an appropriate power supply rating for a typical 50 watt output mobile FM transceiver?
24.0 volts at 4 amperes
13.8 volts at 4 amperes
24.0 volts at 12 amperes
13.8 volts at 12 amperes
T4A01 HRLM (5 - 16)

## Slide 2: Which of the following is an appropriate power supply rating for a typical 50 watt output mobile FM transceiver?
24.0 volts at 4 amperes
13.8 volts at 4 amperes
24.0 volts at 12 amperes
13.8 volts at 12 amperes
(D) T4A01 HRLM (5 - 16)

## Slide 3: Which of the following should be considered when selecting an accessory SWR meter?
The frequency and power level at which the measurements will be made
The distance that the meter will be located from the antenna
The types of modulation being used at the station
All these choices are correct
T4A02 HRLM (4 - 10)

## Slide 4: Which of the following should be considered when selecting an accessory SWR meter?
The frequency and power level at which the measurements will be made
The distance that the meter will be located from the antenna
The types of modulation being used at the station
All these choices are correct
(A) T4A02 HRLM (4 - 10)

## Slide 5: Why are short, heavy-gauge wires used for a transceiver’s DC power connection?
To minimize voltage drop when transmitting
To provide a good counterpoise for the antenna
To avoid RF interference
All of these choices are correct
T4A03 HRLM (5 - 17)

## Slide 6: Why are short, heavy-gauge wires used for a transceiver’s DC power connection?
To minimize voltage drop when transmitting
To provide a good counterpoise for the antenna
To avoid RF interference
All of these choices are correct
(A) T4A03 HRLM (5 - 17)

## Slide 7: How are the transceiver audio input and output connected in a station configured to operate using FT8?
To a computer running a terminal program and connected to a terminal node controller unit
To the audio input and output of a computer running WSJT-X software
To an FT8 conversion unit, a keyboard, and a computer monitor
To a computer connected to the FT8converter.com website
T4A04 HRLM (5 - 14)

## Slide 8: How are the transceiver audio input and output connected in a station configured to operate using FT8?
To a computer running a terminal program and connected to a terminal node controller unit
To the audio input and output of a computer running WSJT-X software
To an FT8 conversion unit, a keyboard, and a computer monitor
To a computer connected to the FT8converter.com website
(B) T4A04 HRLM (5 - 14)

## Slide 9: Where should an RF power meter be installed?
A. In the feed line, between the transmitter and antenna
B. At the power supply output
C. In parallel with the push-to-talk line and the antenna
D. In the power supply cable, as close as possible to the radio
T4A05 HRLM (4 - 18)

## Slide 10: Where should an RF power meter be installed?
A. In the feed line, between the transmitter and antenna
B. At the power supply output
C. In parallel with the push-to-talk line and the antenna
D. In the power supply cable, as close as possible to the radio
(A) T4A05 HRLM (4 - 18)

## Slide 11: What signals are used in a computer-radio interface for digital mode operation?
A. Receive and transmit mode, status, and location
B. Antenna and RF power
C. Receive audio, transmit audio, and push-to-talk (PTT)
D. NMEA GPS location and DC power
T4A06 HRLM (5 - 14)

## Slide 12: What signals are used in a computer-radio interface for digital mode operation?
A. Receive and transmit mode, status, and location
B. Antenna and RF power
C. Receive audio, transmit audio, and push-to-talk (PTT)
D. NMEA GPS location and DC power
(C) T4A06 HRLM (5 - 14)

## Slide 13: Which of the following connections is made between a computer and a transceiver to use computer software when operating digital modes?
Computer “line out” to transceiver push-to-talk
Computer “line in” to transceiver push-to-talk
Computer “line in” to transceiver speaker connector
Computer “line out” to transceiver speaker connector
T4A07 HRLM (5 - 14)

## Slide 14: Which of the following connections is made between a computer and a transceiver to use computer software when operating digital modes?
Computer “line out” to transceiver push-to-talk
Computer “line in” to transceiver push-to-talk
Computer “line in” to transceiver speaker connector
Computer “line out” to transceiver speaker connector
(C) T4A07 HRLM (5 - 14)

## Slide 15: Which of the following conductors is preferred for bonding at RF?
Copper braid removed from coaxial cable
Steel wire
Twisted-pair cable
Flat strap
T4A08 HRLM (9 - 6)

## Slide 16: Which of the following conductors is preferred for bonding at RF?
Copper braid removed from coaxial cable
Steel wire
Twisted-pair cable
Flat strap
(D) T4A08 HRLM (9 - 6)

## Slide 17: How can you determine the length of time that equipment can be powered from a battery?
Divide the watt-hour rating of the battery by the peak power consumption of the equipment
Divide the battery ampere-hour rating by the average current draw of the equipment
Multiply the watts per hour consumed by the equipment by the battery power rating
Multiply the square of the current rating of the battery by the input resistance of the equipment
T4A09 HRLM (5 - 17)

## Slide 18: How can you determine the length of time that equipment can be powered from a battery?
Divide the watt-hour rating of the battery by the peak power consumption of the equipment
Divide the battery ampere-hour rating by the average current draw of the equipment
Multiply the watts per hour consumed by the equipment by the battery power rating
Multiply the square of the current rating of the battery by the input resistance of the equipment
(B) T4A09 HRLM (5 - 17)

## Slide 19: What function is performed with a transceiver and a digital mode hot spot?
Communication using digital voice or data systems via the internet
FT8 digital communications via AFSK
RTTY encoding and decoding without a computer
High-speed digital communications for meteor scatter
T4A10 HRLM (6 - 13)

## Slide 20: What function is performed with a transceiver and a digital mode hot spot?
Communication using digital voice or data systems via the internet
FT8 digital communications via AFSK
RTTY encoding and decoding without a computer
High-speed digital communications for meteor scatter
(A) T4A10 HRLM (6 - 13)

## Slide 21: Where should the negative power return of a mobile transceiver be connected in a vehicle?
A. At the 12-volt battery chassis ground
B. At the antenna mount
C. To any metal part of the vehicle
D. Through the transceiver’s mounting bracket
T4A11 HRLM (5 - 17)

## Slide 22: Where should the negative power return of a mobile transceiver be connected in a vehicle?
A. At the 12-volt battery chassis ground
B. At the antenna mount
C. To any metal part of the vehicle
D. Through the transceiver’s mounting bracket
(A) T4A11 HRLM (5 - 17)