## Slide 1: Why is the benefit of low SWR?
A. Reduced television interference
B. Reduced signal loss
C. Less antenna wear
D. All of these choices are correct
T9B01 HRLM (4 - 10)

## Slide 2: Why is the benefit of low SWR?
A. Reduced television interference
B. Reduced signal loss
C. Less antenna wear
D. All of these choices are correct
(B) T9B01 HRLM (4 - 10)

## Slide 3: What is the most common coaxial cables used in amateur radio installations?
A. 8 ohms
B. 50 ohms
C. 600 ohms
D. 12 ohms
T9B02 HRLM (4 - 9)

## Slide 4: What is the most common coaxial cables used in amateur radio installations?
A. 8 ohms
B. 50 ohms
C. 600 ohms
D. 12 ohms
(B) T9B02 HRLM (4 - 9)

## Slide 5: Why is coaxial cable the most common feed line selected for amateur radio antenna systems?
A. It is easy to use and requires few special installation considerations
B. It has less loss than any other type of feed line
C. It can handle more power than any other type of feed line
D. It is less expensive than any other type of feed line
T9B03 HRLM (4 - 9)

## Slide 6: Why is coaxial cable the most common feed line selected for amateur radio antenna systems?
A. It is easy to use and requires few special installation considerations
B. It has less loss than any other type of feed line
C. It can handle more power than any other type of feed line
D. It is less expensive than any other type of feed line
(A) T9B03 HRLM (4 - 9)

## Slide 7: What is the major function of an antenna tuner (antenna coupler)?
A. It matches the antenna system impedance to the transceiver's output impedance
B. It helps a receiver automatically tune in weak stations
C. It allows an antenna to be used on both transmit and receive
D. It automatically selects the proper antenna for the frequency band being used
T9B04 HRLM (4 - 18)

## Slide 8: What is the major function of an antenna tuner (antenna coupler)?
A. It matches the antenna system impedance to the transceiver's output impedance
B. It helps a receiver automatically tune in weak stations
C. It allows an antenna to be used on both transmit and receive
D. It automatically selects the proper antenna for the frequency band being used
(A) T9B04 HRLM (4 - 18)

## Slide 9: What happens as the frequency of a signal in coaxial cable is increased?
A. The characteristic impedance decreases
B. The loss decreases
C. The characteristic impedance increases
D. The loss increases
T9B05 HRLM (4 - 9)

## Slide 10: What happens as the frequency of a signal in coaxial cable is increased?
A. The characteristic impedance decreases
B. The loss decreases
C. The characteristic impedance increases
D. The loss increases
(D) T9B05 HRLM (4 - 9)

## Slide 11: Which of the following RF connectors types is most suitable for frequencies above 400 MHz?
A. UHF (PL-259/SO-239)
B. Type N
C. RS-213
D. DB-25
T9B06 HRLM (4 - 17)

## Slide 12: Which of the following RF connectors types is most suitable for frequencies above 400 MHz?
A. UHF (PL-259/SO-239)
B. Type N
C. RS-213
D. DB-25
(B) T9B06 HRLM (4 - 17)

## Slide 13: Which of the following is true of PL-259 type coax connectors?
A. They are preferred for microwave operation
B. They are watertight
C. They are commonly used at HF frequencies
D. They are a bayonet type connector
T9B07 HRLM (4 - 17)

## Slide 14: Which of the following is true of PL-259 type coax connectors?
A. They are preferred for microwave operation
B. They are watertight
C. They are commonly used at HF frequencies
D. They are a bayonet type connector
(C) T9B07 HRLM (4 - 17)

## Slide 15: Which of the following is a source of loss in coaxial feed line?
Water intrusion into coaxial connectors
High SWR
Multiple connectors in the line
All these choices are correct
T9B08 HRLM (4 - 17)

## Slide 16: Which of the following is a source of loss in coaxial feed line?
Water intrusion into coaxial connectors
High SWR
Multiple connectors in the line
All these choices are correct
(D) T9B08 HRLM (4 - 17)

## Slide 17: What can cause erratic changes in SWR readings?
A. Local thunderstorm
B. Loose connection in an antenna or a feed line
C. Over-modulation
D. Overload from a strong local station
T9B09 HRLM (4 - 10)

## Slide 18: What can cause erratic changes in SWR readings?
A. Local thunderstorm
B. Loose connection in an antenna or a feed line
C. Over-modulation
D. Overload from a strong local station
(B) T9B09 HRLM (4 - 10)

## Slide 19: What is the electrical difference between RG-58 and RG-213 coaxial cable?
A. There is no significant difference between the two types
B. RG-58 cable has two shields
C. RG-213 cable has less loss at a given frequency
D. RG-58 cable can handle higher power levels
T9B10 HRLM (4 - 17)

## Slide 20: What is the electrical difference between RG-58 and RG-213 coaxial cable?
A. There is no significant difference between the two types
B. RG-58 cable has two shields
C. RG-213 cable has less loss at a given frequency
D. RG-58 cable can handle higher power levels
(C) T9B10 HRLM (4 - 17)

## Slide 21: Which of the following types of feed line has the lowest loss at VHF and UHF?
A. 50-ohm flexible coax
B. Multi-conductor unbalanced cable
C. Air-insulated hard line
D. 75-ohm flexible coax
T9B11 HRLM (4 - 17)

## Slide 22: Which of the following types of feed line has the lowest loss at VHF and UHF?
A. 50-ohm flexible coax
B. Multi-conductor unbalanced cable
C. Air-insulated hard line
D. 75-ohm flexible coax
(C) T9B11 HRLM (4 - 17)