## Slide 1: What is the primary purpose of a dummy load?
A. To prevent transmitting signals over the air when making tests
B. To prevent over-modulation of a transmitter
C. To improve the efficiency of an antenna
D. To improve the signal-to-noise ratio of a receiver
T7C01 HRLM (5 - 7)

## Slide 2: What is the primary purpose of a dummy load?
A. To prevent transmitting signals over the air when making tests
B. To prevent over-modulation of a transmitter
C. To improve the efficiency of an antenna
D. To improve the signal-to-noise ratio of a receiver
(A) T7C01 HRLM (5 - 7)

## Slide 3: Which of the following can be used to determine if an antenna is resonant at the desired operating frequency?
A. A VTVM
B. An antenna analyzer
C. A Q meter
D. A frequency counter
T7C02 HRLM (4 - 18)

## Slide 4: Which of the following can be used to determine if an antenna is resonant at the desired operating frequency?
A. A VTVM
B. An antenna analyzer
C. A Q meter
D. A frequency counter
(B) T7C02 HRLM (4 - 18)

## Slide 5: What does a dummy load consist of?
A high-gain amplifier and a TR switch
A non-inductive resistor mounted on a heat sink
A low-voltage power supply and a DC relay
A 50-ohm reactance used to terminate a transmission line
T7C03 HRLM (5 - 7)

## Slide 6: What does a dummy load consist of?
A high-gain amplifier and a TR switch
A non-inductive resistor mounted on a heat sink
A low-voltage power supply and a DC relay
A 50-ohm reactance used to terminate a transmission line
(B) T7C03 HRLM (5 - 7)

## Slide 7: What reading on an SWR meter indicates a perfect impedance match between the antenna and the feed line?
50:50
Zero
1:1
Full Scale
T7C04 HRLM (4 - 10)

## Slide 8: What reading on an SWR meter indicates a perfect impedance match between the antenna and the feed line?
50:50
Zero
1:1
Full Scale
(C) T7C04 HRLM (4 - 10)

## Slide 9: Why do most solid-state amateur radio transmitters reduce output power as SWR increases?
A. To protect the output amplifier transistors
B. To comply with FCC rules on spectral purity
C. Because power supplies cannot supply enough current at high SWR
D. To lower the SWR on the transmission line
T7C05 HRLM (4 - 10)

## Slide 10: Why do most solid-state amateur radio transmitters reduce output power as SWR increases?
A. To protect the output amplifier transistors
B. To comply with FCC rules on spectral purity
C. Because power supplies cannot supply enough current at high SWR
D. To lower the SWR on the transmission line
(A) T7C05 HRLM (4 - 10)

## Slide 11: What does an SWR reading of 4:1 indicate?
A. Loss of -4 dB
B. Good impedance match
C. Gain of +4 dB
D. Impedance mismatch
T7C06 HRLM (4 - 10)

## Slide 12: What does an SWR reading of 4:1 indicate?
A. Loss of -4 dB
B. Good impedance match
C. Gain of +4 dB
D. Impedance mismatch
(D) T7C06 HRLM (4 - 10)

## Slide 13: What happens to power lost in a feed line?
A. It increases the SWR
B. It is radiated as harmonics
C. It is converted into heat
D. It distorts of your signal
T7C07 HRLM (4 - 9)

## Slide 14: What happens to power lost in a feed line?
A. It increases the SWR
B. It is radiated as harmonics
C. It is converted into heat
D. It distorts of your signal
(C) T7C07 HRLM (4 - 9)

## Slide 15: Which instrument can be used to determine SWR?
A. Voltmeter
B. Ohmmeter
C. Iambic pentameter
D. Directional wattmeter
T7C08 HRLM (4 - 18)

## Slide 16: Which instrument can be used to determine SWR?
A. Voltmeter
B. Ohmmeter
C. Iambic pentameter
D. Directional wattmeter
(D) T7C08 HRLM (4 - 18)

## Slide 17: Which of the following causes failure of coaxial cables?
A. Moisture contamination
B. Solder flux contamination
C. Rapid fluctuation in transmitter output power
D. Operation at 100% duty cycle for an extended period
T7C09 HRLM (4 - 17)

## Slide 18: Which of the following causes failure of coaxial cables?
A. Moisture contamination
B. Solder flux contamination
C. Rapid fluctuation in transmitter output power
D. Operation at 100% duty cycle for an extended period
(A) T7C09 HRLM (4 - 17)

## Slide 19: Why should the outer jacket of coaxial cable be resistant to ultraviolet light?
A. Ultraviolet resistant jackets prevent harmonic radiation
B. Ultraviolet light can increase losses in the cable’s jacket
C. Ultraviolet and RF signals can mix, causing interference
D. Ultraviolet light can damage the jacket and allow water to enter the cable
T7C10 HRLM (4 - 17)

## Slide 20: Why should the outer jacket of coaxial cable be resistant to ultraviolet light?
A. Ultraviolet resistant jackets prevent harmonic radiation
B. Ultraviolet light can increase losses in the cable’s jacket
C. Ultraviolet and RF signals can mix, causing interference
D. Ultraviolet light can damage the jacket and allow water to enter the cable
(D) T7C10 HRLM (4 - 17)

## Slide 21: What is a disadvantage of air core coaxial cable when compared to foam or solid dielectric types?
A. It has more loss per foot
B. It cannot be used for VHF or UHF antennas
C. It requires special techniques to prevent moisture in the cable
D. It cannot be used at below freezing temperatures
T7C11 HRLM (4 - 17)

## Slide 22: What is a disadvantage of air core coaxial cable when compared to foam or solid dielectric types?
A. It has more loss per foot
B. It cannot be used for VHF or UHF antennas
C. It requires special techniques to prevent moisture in the cable
D. It cannot be used at below freezing temperatures
(C) T7C11 HRLM (4 - 17)