## Slide 1: What is a beam antenna?
A. An antenna built from aluminum I-beams
B. An omnidirectional antenna invented by Clarence Beam
C. An antenna that concentrates signals in one direction
D. An antenna that reverses the phase of received signals
T9A01 HRLM (4 - 15)

## Slide 2: What is a beam antenna?
A. An antenna built from aluminum I-beams
B. An omnidirectional antenna invented by Clarence Beam
C. An antenna that concentrates signals in one direction
D. An antenna that reverses the phase of received signals
(C) T9A01 HRLM (4 - 15)

## Slide 3: Which of the following describes a type of antenna loading?
Electrically lengthening by inserting inductors in radiating elements
Inserting a resistor in the radiating portion of the antenna to make it resonant
C. Installing a spring in the base of a mobile vertical antenna to make it more flexible
D. Strengthening the radiating elements of a beam antenna to better resist wind damage
T9A02 HRLM (4 - 12)

## Slide 4: Which of the following describes a type of antenna loading?
A. Electrically lengthening by inserting inductors in radiating elements
B. Inserting a resistor in the radiating portion of the antenna to make it resonant
C. Installing a spring in the base of a mobile vertical antenna to make it more flexible
D. Strengthening the radiating elements of a beam antenna to better resist wind damage
(A) T9A02 HRLM (4 - 12)

## Slide 5: Which of the following describes a simple dipole oriented parallel to the Earth's surface?
A. A ground-wave antenna
B. A horizontally polarized antenna
C. A travelling-wave antenna
D. A vertically polarized antenna
T9A03 HRLM (4 - 12)

## Slide 6: Which of the following describes a simple dipole oriented parallel to the Earth's surface?
A. A ground-wave antenna
B. A horizontally polarized antenna
C. A travelling-wave antenna
D. A vertically polarized antenna
(B) T9A03 HRLM (4 - 12)

## Slide 7: What is a disadvantage of the short, flexible antenna supplied with most handheld radio transceivers when compared to a full-sized quarter-wave antenna?
A. It has low efficiency
B. It transmits only circularly polarized signals
C. It is mechanically fragile
D. All of these choices are correct
T9A04 HRLM (4 - 12)

## Slide 8: What is a disadvantage of the short, flexible antenna supplied with most handheld radio transceivers when compared to a full-sized quarter-wave antenna?
A. It has low efficiency
B. It transmits only circularly polarized signals
C. It is mechanically fragile
D. All of these choices are correct
(A) T9A04 HRLM (4 - 12)

## Slide 9: Which of the following increases the resonant frequency of a dipole antenna?
A. Lengthening it
B. Insert coils in series with radiating wires
C. Shortening it
D. Add capacitive loading to the ends of the radiating wires
T9A05 HRLM (4 - 12)

## Slide 10: Which of the following increases the resonant frequency of a dipole antenna?
A. Lengthening it
B. Insert coils in series with radiating wires
C. Shortening it
D. Add capacitive loading to the ends of the radiating wires
(C) T9A05 HRLM (4 - 12)

## Slide 11: Which of the following types of antenna offers the greatest gain?
5/8 wave vertical
Isotropic
J pole
Yagi
T9A06 HRLM (4 - 15)

## Slide 12: Which of the following types of antenna offers the greatest gain?
5/8 wave vertical
Isotropic
J pole
Yagi
(D) T9A06 HRLM (4 - 15)

## Slide 13: What is a disadvantage of using a handheld VHF transceiver with its flexible antenna inside a vehicle?
A. Signal strength is reduced due to the shielding effect of the vehicle
B. The bandwidth of the antenna will decrease, increasing SWR
C. The SWR might decrease, decreasing the signal strength
D. All of these choices are correct
T9A07 HRLM (4 - 12)

## Slide 14: What is a disadvantage of using a handheld VHF transceiver with its flexible antenna inside a vehicle?
A. Signal strength is reduced due to the shielding effect of the vehicle
B. The bandwidth of the antenna will decrease, increasing SWR
C. The SWR might decrease, decreasing the signal strength
D. All of these choices are correct
(A) T9A07 HRLM (4 - 12)

## Slide 15: What is the approximate length, in inches, of a quarter-wavelength vertical antenna for 146 MHz?
A. 112
B. 50
C. 19
D. 12
T9A08 HRLM (4 - 12)

## Slide 16: What is the approximate length, in inches, of a quarter-wavelength vertical antenna for 146 MHz?
A. 112
B. 50
C. 19
D. 12
(C) T9A08 HRLM (4 - 12)

## Slide 17: What is the approximate length, in inches, of a half-wavelength 6 meter dipole antenna?
A. 6
B. 50
C. 112
D. 236
T9A09 HRLM (4 - 12)

## Slide 18: What is the approximate length, in inches, of a half-wavelength 6 meter dipole antenna?
A. 6
B. 50
C. 112
D. 236
(C) T9A09 HRLM (4 - 12)

## Slide 19: In which direction does a half-wave dipole antenna radiate the strongest signal?
A. Equally in all directions
B. Off the ends of the antenna
C. In the direction of the feed line
D. Broadside to the antenna
T9A10 HRLM (4 - 12)

## Slide 20: In which direction does a half-wave dipole antenna radiate the strongest signal?
A. Equally in all directions
B. Off the ends of the antenna
C. In the direction of the feed line
D. Broadside to the antenna
(D) T9A10 HRLM (4 - 12)

## Slide 21: What is antenna gain?
A. The additional power that is added to the transmitter power
B. The additional power that is required in the antenna when transmitting on a higher frequency
C. The increase in signal strength in a specified direction compared to a reference antenna
D. The increase in impedance on receive or transmit compared to a reference antenna
T9A11 HRLM (4 - 7)

## Slide 22: What is antenna gain?
A. The additional power that is added to the transmitter power
B. The additional power that is required in the antenna when transmitting on a higher frequency
C. The increase in signal strength in a specified direction compared to a reference antenna
D. The increase in impedance on receive or transmit compared to a reference antenna
(C) T9A11 HRLM (4 - 7)

## Slide 23: What is an advantage of a 5/8 wavelength whip antenna for VHF or UHF mobile service?
A. It has more gain than a 1/4 wavelength antenna
B. It radiates at a very high angle
C. It eliminates distortion caused by reflected signals
D. It has 10 times the power gain of a 1/4 wavelength design
T9A12 HRLM (4 - 12)

## Slide 24: What is an advantage of a 5/8 wavelength whip antenna for VHF or UHF mobile service?
A. It has more gain than a 1/4 wavelength antenna
B. It radiates at a very high angle
C. It eliminates distortion caused by reflected signals
D. It has 10 times the power gain of a 1/4 wavelength design
(A) T9A12 HRLM (4 - 12)