## Slide 1: Which term describes the ability of a receiver to detect the presence of a signal?
A. Linearity
B. Sensitivity
C. Selectivity
D. Total Harmonic Distortion
T7A01 HRLM (5 - 9)

## Slide 2: Which term describes the ability of a receiver to detect the presence of a signal?
A. Linearity
B. Sensitivity
C. Selectivity
D. Total Harmonic Distortion
(B) T7A01 HRLM (5 - 9)

## Slide 3: What is a transceiver?
A. A device that combines a receiver and transmitter
B. A device for matching feed line impedance to 50 ohms
C. A device for automatically sending and decoding Morse code
D. A device for converting receiver and transmitter frequencies to another band
T7A02 HRLM (2 - 7)

## Slide 4: What is a transceiver?
A. A device that combines a receiver and transmitter
B. A device for matching feed line impedance to 50 ohms
C. A device for automatically sending and decoding Morse code
D. A device for converting receiver and transmitter frequencies to another band
(A) T7A02 HRLM (2 - 7)

## Slide 5: Which of the following is used to convert a signal from one frequency to another?
A. Phase splitter
B. Mixer
C. Inverter
D. Amplifier
T7A03 HRLM (3 - 18)

## Slide 6: Which of the following is used to convert a signal from one frequency to another?
A. Phase splitter
B. Mixer
C. Inverter
D. Amplifier
(B) T7A03 HRLM (3 - 18)

## Slide 7: Which term describes the ability of a receiver to discriminate between multiple signals?
A. Discrimination ratio
B. Sensitivity
C. Selectivity
D. Harmonic distortion
T7A04 HRLM (5 - 9)

## Slide 8: Which term describes the ability of a receiver to discriminate between multiple signals?
A. Discrimination ratio
B. Sensitivity
C. Selectivity
D. Harmonic distortion
(C) T7A04 HRLM (5 - 9)

## Slide 9: What is the name of a circuit that generates a signal at a specific frequency?
A. Reactance modulator
B. Product detector
C. Low-pass filter
D. Oscillator
T7A05 HRLM (3 - 17)

## Slide 10: What is the name of a circuit that generates a signal at a specific frequency?
A. Reactance modulator
B. Product detector
C. Low-pass filter
D. Oscillator
(D) T7A05 HRLM (3 - 17)

## Slide 11: What device converts the RF input and output of a transceiver to another band?
A. High-pass filter
B. Low-pass filter
C. Transverter
D. Phase converter
T7A06 HRLM (5 - 11)

## Slide 12: What device converts the RF input and output of a transceiver to another band?
A. High-pass filter
B. Low-pass filter
C. Transverter
D. Phase converter
(C) T7A06 HRLM (5 - 11)

## Slide 13: What is the function of a transceiver’s “PTT” input?
Input for a key used to send CW
Switches transceiver from receive to transmit when grounded
Provides a transmit tuning tone when grounded
Input for a preamplifier tuning tone
T7A07 HRLM (5 - 7)

## Slide 14: What is the function of a transceiver’s “PTT” input?
Input for a key used to send CW
Switches transceiver from receive to transmit when grounded
Provides a transmit tuning tone when grounded
Input for a preamplifier tuning tone
(B) T7A07 HRLM (5 - 7)

## Slide 15: Which of the following describes combining speech with an RF carrier signal?
A. Impedance matching
B. Oscillation
C. Modulation
D. Low-pass filtering
T7A08 HRLM (3 - 17)

## Slide 16: Which of the following describes combining speech with an RF carrier signal?
A. Impedance matching
B. Oscillation
C. Modulation
D. Low-pass filtering
(C) T7A08 HRLM (3 - 17)

## Slide 17: What is the function of the SSB/CW-FM switch on a VHF power amplifier?
A. Change the mode of the transmitted signal
B. Set the amplifier for proper operation in the selected mode
C. Change the frequency range of the amplifier to operate in the proper portion of the band
D. Reduce the received signal noise
T7A09 HRLM (5 - 10)

## Slide 18: What is the function of the SSB/CW-FM switch on a VHF power amplifier?
A. Change the mode of the transmitted signal
B. Set the amplifier for proper operation in the selected mode
C. Change the frequency range of the amplifier to operate in the proper portion of the band
D. Reduce the received signal noise
(B) T7A09 HRLM (5 - 10)

## Slide 19: What device increases the low-power output from a transceiver?
A. A voltage divider
B. An RF power amplifier
C. An impedance network
D. All of these choices are correct
T7A10 HRLM (5 - 10)

## Slide 20: What device increases the low-power output from a transceiver?
A. A voltage divider
B. An RF power amplifier
C. An impedance network
D. All of these choices are correct
(B) T7A10 HRLM (5 - 10)

## Slide 21: Where is an RF preamplifier installed?
A. Between the antenna and receiver
B. At the output of the transmitter's power amplifier
C. Between a transmitter and antenna tuner
D. At the receiver's audio output
T7A11 HRLM (5 - 9)

## Slide 22: Where is an RF preamplifier installed?
A. Between the antenna and receiver
B. At the output of the transmitter's power amplifier
C. Between a transmitter and antenna tuner
D. At the receiver's audio output
(A) T7A11 HRLM (5 - 9)