## Slide 1: Why are simplex UHF signals rarely heard beyond their radio horizon?
A. They are too weak to go very far
B. FCC regulations prohibit them from going more than 50 miles
C. UHF signals are usually not reflected by the ionosphere
D. UHF signals are absorbed by the ionospheric D layer
T3C01 HRLM (4 - 3)

## Slide 2: Why are simplex UHF signals rarely heard beyond their radio horizon?
A. They are too weak to go very far
B. FCC regulations prohibit them from going more than 50 miles
C. UHF signals are usually not reflected by the ionosphere
D. UHF signals are absorbed by the ionospheric D layer
(C) T3C01 HRLM (4 - 3)

## Slide 3: What is a characteristic of HF communication compared with communications on VHF and higher frequencies?
A. HF antennas are generally smaller
B. HF accommodates wider bandwidth signals
C. Long distance ionospheric propagation is far more common on HF
D. There is less atmospheric interference (static) on HF
T3C02 HRLM (4 - 3)

## Slide 4: What is a characteristic of HF communication compared with communications on VHF and higher frequencies?
A. HF antennas are generally smaller
B. HF accommodates wider bandwidth signals
C. Long distance ionospheric propagation is far more common on HF
D. There is less atmospheric interference (static) on HF
(C) T3C02 HRLM (4 - 3)

## Slide 5: What is a characteristic of VHF signals received via auroral backscatter?
A. They are often received from distances of 10,000 or more miles
B. They are distorted and signal strength varies considerably
C. They occur only during winter nighttime hours
D. They are generally strongest when your antenna is aimed west
T3C03 HRLM (4 - 3)

## Slide 6: What is a characteristic of VHF signals received via auroral backscatter?
A. They are often received from distances of 10,000 or more miles
B. They are distorted and signal strength varies considerably
C. They occur only during winter nighttime hours
D. They are generally strongest when your antenna is aimed west
(B) T3C03 HRLM (4 - 3)

## Slide 7: Which of the following types of propagation is most commonly associated with occasional strong signals on the 10, 6, and 2 meter bands from beyond the radio horizon?
A. Backscatter
B. Sporadic E
C. D region absorption
D. Gray-line propagation
T3C04 HRLM (4 - 3)

## Slide 8: Which of the following types of propagation is most commonly associated with occasional strong signals on the 10, 6, and 2 meter bands from beyond the radio horizon?
A. Backscatter
B. Sporadic E
C. D region absorption
D. Gray-line propagation
(B) T3C04 HRLM (4 - 3)

## Slide 9: Which of the following effects may allow radio signals to travel beyond obstructions between the transmitting and receiving stations?
A. Knife-edge diffraction
B. Faraday rotation
C. Quantum tunneling
D. Doppler shift
T3C05 HRLM (4 - 1)

## Slide 10: Which of the following effects may allow radio signals to travel beyond obstructions between the transmitting and receiving stations?
A. Knife-edge diffraction
B. Faraday rotation
C. Quantum tunneling
D. Doppler shift
(A) T3C05 HRLM (4 - 1)

## Slide 11: What type of propagation is responsible for allowing over-the-horizon VHF and UHF communications to ranges of approximately 300 miles on a regular basis?
A. Tropospheric ducting
B. D layer refraction
C. F2 layer refraction
D. Faraday rotation
T3C06 HRLM (4 - 1)

## Slide 12: What type of propagation is responsible for allowing over-the-horizon VHF and UHF communications to ranges of approximately 300 miles on a regular basis?
A. Tropospheric ducting
B. D layer refraction
C. F2 layer refraction
D. Faraday rotation
(A) T3C06 HRLM (4 - 1)

## Slide 13: What band is best suited for communicating via meteor scatter?
A. 33 centimeters
B. 6 meters
C. 2 meters
D. 70 centimeters
T3C07 HRLM (4 - 3)

## Slide 14: What band is best suited for communicating via meteor scatter?
A. 33 centimeters
B. 6 meters
C. 2 meters
D. 70 centimeters
(B) T3C07 HRLM (4 - 3)

## Slide 15: What causes tropospheric ducting?
A. Discharges of lightning during electrical storms
B. Sunspots and solar flares
C. Updrafts from hurricanes and tornadoes
D. Temperature inversions in the atmosphere
T3C08 HRLM (4 - 2)

## Slide 16: What causes tropospheric ducting?
A. Discharges of lightning during electrical storms
B. Sunspots and solar flares
C. Updrafts from hurricanes and tornadoes
D. Temperature inversions in the atmosphere
(D) T3C08 HRLM (4 - 2)

## Slide 17: What is generally the best time for long-distance 10 meter band propagation via the F layer?
A. From dawn to shortly after sunset during periods of high sunspot activity
B. From shortly after sunset to dawn during periods of high sunspot activity
C. From dawn to shortly after sunset during periods of low sunspot activity
D. From shortly after sunset to dawn during periods of low sunspot activity
T3C09 HRLM (4 - 3)

## Slide 18: What is generally the best time for long-distance 10 meter band propagation via the F layer?
A. From dawn to shortly after sunset during periods of high sunspot activity
B. From shortly after sunset to dawn during periods of high sunspot activity
C. From dawn to shortly after sunset during periods of low sunspot activity
D. From shortly after sunset to dawn during periods of low sunspot activity
(A) T3C09 HRLM (4 - 3)

## Slide 19: Which of the following bands may provide long distance communications via the ionosphere’s F region during the peak of the sunspot cycle?
A. 6 or 10 meter bands
B. 23 centimeter band
C. 70 centimeter or 1.25 meter bands
D. All of these choices are correct
T3C10 HRLM (4 - 3)

## Slide 20: Which of the following bands may provide long distance communications via the ionosphere’s F region during the peak of the sunspot cycle?
A. 6 or 10 meter bands
B. 23 centimeter band
C. 70 centimeter or 1.25 meter bands
D. All of these choices are correct
(A) T3C10 HRLM (4 - 3)

## Slide 21: Why is the radio horizon for VHF and UHF signals more distant than the visual horizon?
A. Radio signals move somewhat faster than the speed of light
B. Radio waves are not blocked by dust particles
C. The atmosphere refracts radio waves slightly
D. Radio waves are blocked by dust particles
T3C11 HRLM (4 - 2)

## Slide 22: Why is the radio horizon for VHF and UHF signals more distant than the visual horizon?
A. Radio signals move somewhat faster than the speed of light
B. Radio waves are not blocked by dust particles
C. The atmosphere refracts radio waves slightly
D. Radio waves are blocked by dust particles
(C) T3C11 HRLM (4 - 2)