## Slide 1: Why do VHF signal strengths sometimes vary greatly when the antenna is moved only a few feet?
The signal path encounters different concentrations of water vapor
VHF ionospheric propagation is very sensitive to path length
Multipath propagation cancels or reinforces signals
All these choices are correct
T3A01 HRLM (4 - 1)

## Slide 2: Why do VHF signal strengths sometimes vary greatly when the antenna is moved only a few feet?
The signal path encounters different concentrations of water vapor
VHF ionospheric propagation is very sensitive to path length
Multipath propagation cancels or reinforces signals
All these choices are correct
(C) T3A01 HRLM (4 - 1)

## Slide 3: What is the effect of vegetation on UHF and microwave signals?
Knife-edge diffraction
Absorption
Amplification
Polarization rotation
T3A02 HRLM (4 - 1)

## Slide 4: What is the effect of vegetation on UHF and microwave signals?
Knife-edge diffraction
Absorption
Amplification
Polarization rotation
(B) T3A02 HRLM (4 - 1)

## Slide 5: What antenna polarization is normally used for long-distance weak-signal CW and SSB contacts using the VHF and UHF bands?
A. Right-hand circular
B. Left-hand circular
C. Horizontal
D. Vertical
T3A03 HRLM (4 - 16)

## Slide 6: What antenna polarization is normally used for long-distance weak-signal CW and SSB contacts using the VHF and UHF bands?
A. Right-hand circular
B. Left-hand circular
C. Horizontal
D. Vertical
(C) T3A03 HRLM (4 - 16)

## Slide 7: What happens if the antennas at opposite ends of a VHF or UHF line of sight radio link are not using the same polarization?
A. The modulation sidebands might become inverted
B. Signals could be significantly weaker
C. Signals have an echo effect
D. Nothing significant will happen
T3A04 HRLM (4 - 5)

## Slide 8: What happens if the antennas at opposite ends of a VHF or UHF line of sight radio link are not using the same polarization?
A. The modulation sidebands might become inverted
B. Signals could be significantly weaker
C. Signals have an echo effect
D. Nothing significant will happen
(B) T3A04 HRLM (4 - 5)

## Slide 9: When using a directional antenna, how might your station be able to access a distant repeater if buildings or obstructions are blocking the direct line of sight path?
A. Change from vertical to horizontal polarization
B. Try to find a path that reflects signals to the repeater
C. Try the long path
D. Increase the antenna SWR
T3A05 HRLM (4 - 15)

## Slide 10: When using a directional antenna, how might your station be able to access a distant repeater if buildings or obstructions are blocking the direct line of sight path?
A. Change from vertical to horizontal polarization
B. Try to find a path that reflects signals to the repeater
C. Try the long path
D. Increase the antenna SWR
(B) T3A05 HRLM (4 - 15)

## Slide 11: What is the meaning of the term “picket fencing”?
Alternating transmissions during a net operation
Rapid flutter on mobile signals due to multipath propagation
A type of ground system used with vertical antennas
Local vs long-distance communications
T3A06 HRLM (4 - 1)

## Slide 12: What is the meaning of the term “picket fencing”?
Alternating transmissions during a net operation
Rapid flutter on mobile signals due to multipath propagation
A type of ground system used with vertical antennas
Local vs long-distance communications
(B) T3A06 HRLM (4 - 1)

## Slide 13: What weather condition might decrease range at microwave frequencies?
High winds
Low barometric pressure
Precipitation
Colder temperatures
T3A07 HRLM (4 - 1)

## Slide 14: What weather condition might decrease range at microwave frequencies?
High winds
Low barometric pressure
Precipitation
Colder temperatures
(C) T3A07 HRLM (4 - 1)

## Slide 15: What is a likely cause of irregular fading of signals received by ionospheric reflection?
A. Frequency shift due to Faraday rotation
B. Interference from thunderstorms
C. Intermodulation distortion
D. Random combining of signals arriving via different paths
T3A08 HRLM (4 - 1)

## Slide 16: What is a likely cause of irregular fading of signals received by ionospheric reflection?
A. Frequency shift due to Faraday rotation
B. Interference from thunderstorms
C. Intermodulation distortion
D. Random combining of signals arriving via different paths
(D) T3A08 HRLM (4 - 1)

## Slide 17: Which of the following results from the fact that signals propagated from the ionosphere are elliptically polarized?
A. Digital modes are unusable
B. Either vertically or horizontally polarized antennas may be used for transmission or reception
C. FM voice is unusable
D. Both the transmitting and receiving antennas must be of the same polarization
T3A09 HRLM (4 - 5)

## Slide 18: Which of the following results from the fact that signals propagated from the ionosphere are elliptically polarized?
A. Digital modes are unusable
B. Either vertically or horizontally polarized antennas may be used for transmission or reception
C. FM voice is unusable
D. Both the transmitting and receiving antennas must be of the same polarization
(B) T3A09 HRLM (4 - 5)

## Slide 19: What effect does multi-path propagation have on data transmissions?
A. Transmission rates can be increased by a factor equal to the number of separate paths observed
B. Transmission rates must be decreased by a factor equal to the number of separate paths observed
C. No significant changes will occur if the signals are transmitted using FM
D. Error rates are likely to increase
T3A10 HRLM (4 - 1)

## Slide 20: What effect does multi-path propagation have on data transmissions?
A. Transmission rates can be increased by a factor equal to the number of separate paths observed
B. Transmission rates must be decreased by a factor equal to the number of separate paths observed
C. No significant changes will occur if the signals are transmitted using FM
D. Error rates are likely to increase
(D) T3A10 HRLM (4 - 1)

## Slide 21: Which region of the atmosphere can refract or bend HF and VHF radio waves?
A. The stratosphere
B. The troposphere
C. The ionosphere
D. The mesosphere
T3A11 HRLM (4 - 3)

## Slide 22: Which region of the atmosphere can refract or bend HF and VHF radio waves?
A. The stratosphere
B. The troposphere
C. The ionosphere
D. The mesosphere
(C) T3A11 HRLM (4 - 3)

## Slide 23: What is the effect fog and light rain affect radio range on the 10 meter and 6 meter bands?
A. Absorption
B. Little effect
C. Deflection
D. Range increase
T3A12 HRLM (4 - 1)

## Slide 24: What is the effect fog and light rain affect radio range on the 10 meter and 6 meter bands?
A. Absorption
B. Little effect
C. Deflection
D. Range increase
(B) T3A12 HRLM (4 - 1)