## Slide 1: Which of the following is a safety hazard of a 12-volt storage battery?
A. Touching both terminals with the hands can cause electrical shock
B. Shorting the terminals can cause burns, fire, or an explosion
C. RF emissions from a nearby transmitter can cause the electrolyte to emit poison gas
D. All of these choices are correct
T0A01 HRLM (9 - 2)

## Slide 2: Which of the following is a safety hazard of a 12-volt storage battery?
A. Touching both terminals with the hands can cause electrical shock
B. Shorting the terminals can cause burns, fire, or an explosion
C. RF emissions from a nearby transmitter can cause the electrolyte to emit poison gas
D. All of these choices are correct
(B) T0A01 HRLM (9 - 2)

## Slide 3: What health hazard is presented by electrical current flowing through the body?
A. It may cause injury by heating tissue
B. It may disrupt the electrical functions of cells
C. It may cause involuntary muscle contractions
D. All of these choices are correct
T0A02 HRLM (9 - 2)

## Slide 4: What health hazard is presented by electrical current flowing through the body?
A. It may cause injury by heating tissue
B. It may disrupt the electrical functions of cells
C. It may cause involuntary muscle contractions
D. All of these choices are correct
(D) T0A02 HRLM (9 - 2)

## Slide 5: In the United States, what circuit does black wire insulation indicate in a three-wire 120 V cable?
A. Neutral
B. Hot
C. Equipment ground
D. Black insulation is never used
T0A03 HRLM (9 - 4)

## Slide 6: In the United States, what circuit does black wire insulation indicate in a three-wire 120 V cable?
A. Neutral
B. Hot
C. Equipment ground
D. Black insulation is never used
(B) T0A03 HRLM (9 - 4)

## Slide 7: What is the purpose of a fuse in an electrical circuit?
A. To prevent power supply ripple from damaging a circuit
B. To remove power in case of overload
C. To limit current to prevent shocks
D. All of these choices are correct
T0A04 HRLM (3 - 12)

## Slide 8: What is the purpose of a fuse in an electrical circuit?
A. To prevent power supply ripple from damaging a circuit
B. To remove power in case of overload
C. To limit current to prevent shocks
D. All of these choices are correct
(B) T0A04 HRLM (3 - 12)

## Slide 9: Why should a 5-ampere fuse never be replaced with a 20-ampere fuse?
A. The larger fuse would be likely to blow because it is rated for higher current
B. The power supply ripple would greatly increase
C. Excessive current could cause a fire
D. All of these choices are correct
T0A05 HRLM (3 - 12)

## Slide 10: Why should a 5-ampere fuse never be replaced with a 20-ampere fuse?
A. The larger fuse would be likely to blow because it is rated for higher current
B. The power supply ripple would greatly increase
C. Excessive current could cause a fire
D. All of these choices are correct
(C) T0A05 HRLM (3 - 12)

## Slide 11: What is a good way to guard against electrical shock at your station?
A. Use three-wire cords and plugs for all AC powered equipment
B. Connect all AC powered station equipment to a common safety ground
C. Install mechanical interlocks in high-voltage circuits
D. All of these choices are correct
T0A06 HRLM (9 - 4)

## Slide 12: What is a good way to guard against electrical shock at your station?
A. Use three-wire cords and plugs for all AC powered equipment
B. Connect all AC powered station equipment to a common safety ground
C. Install mechanical interlocks in high-voltage circuits
D. All of these choices are correct
(D) T0A06 HRLM (9 - 4)

## Slide 13: Where should a lightning arrester be installed in a coaxial feed line?
At the output connector of a transceiver
At the antenna feed point
At the ac power service panel
On a grounded panel near where feed lines enter the building
T0A07 HRLM (9 - 5)

## Slide 14: Where should a lightning arrester be installed in a coaxial feed line?
At the output connector of a transceiver
At the antenna feed point
At the ac power service panel
On a grounded panel near where feed lines enter the building
(D) T0A07 HRLM (9 - 5)

## Slide 15: Where should a fuse or circuit breaker be installed in a 120V AC power circuit?
In series with the hot conductor only
In series with the hot and neutral conductors
In parallel with the hot conductor only
In parallel with the hot and neutral conductors
T0A08 HRLM (9 - 4)

## Slide 16: Where should a fuse or circuit breaker be installed in a 120V AC power circuit?
In series with the hot conductor only
In series with the hot and neutral conductors
In parallel with the hot conductor only
In parallel with the hot and neutral conductors
(A) T0A08 HRLM (9 - 4)

## Slide 17: What should be done to all external ground rods or earth connections?
A. Waterproof them with silicone caulk or electrical tape
B. Keep them as far apart as possible
C. Bond them together with heavy wire or conductive strap
D. Tune them for resonance on the lowest frequency of operation
T0A09 HRLM (9 - 5)

## Slide 18: What should be done to all external ground rods or earth connections?
A. Waterproof them with silicone caulk or electrical tape
B. Keep them as far apart as possible
C. Bond them together with heavy wire or conductive strap
D. Tune them for resonance on the lowest frequency of operation
(C) T0A09 HRLM (9 - 5)

## Slide 19: What hazard is caused by charging or discharging a battery too quickly?
Overheating or out-gassing
Excess output ripple
Half-wave rectification
Inverse memory effect
T0A10 HRLM (5 - 17)

## Slide 20: What hazard is caused by charging or discharging a battery too quickly?
Overheating or out-gassing
Excess output ripple
Half-wave rectification
Inverse memory effect
(A) T0A10 HRLM (5 - 17)

## Slide 21: What hazard exists in a power supply immediately after turning it off?
Circulating currents in the dc filter
Leakage flux in the power transformer
Voltage transients from kickback diodes
Charge stored in filter capacitors
T0A11 HRLM (9 - 2)

## Slide 22: What hazard exists in a power supply immediately after turning it off?
Circulating currents in the dc filter
Leakage flux in the power transformer
Voltage transients from kickback diodes
Charge stored in filter capacitors
(D) T0A11 HRLM (9 - 2)