## Slide 1: What can you do if you are told your FM handheld or mobile transceiver is over-deviating?
A. Talk louder into the microphone
B. Let the transceiver cool off
C. Change to a higher power level
D. Talk farther away from the microphone
T7B01 HRLM (5 - 8)

## Slide 2: What can you do if you are told your FM handheld or mobile transceiver is over-deviating?
A. Talk louder into the microphone
B. Let the transceiver cool off
C. Change to a higher power level
D. Talk farther away from the microphone
(D) T7B01 HRLM (5 - 8)

## Slide 3: What would cause a broadcast AM or FM radio to receive an amateur radio transmission unintentionally?
A. The receiver is unable to reject strong signals outside the AM or FM band
B. The microphone gain of the transmitter is turned up too high
C. The audio amplifier of the transmitter is overloaded
D. The deviation of an FM transmitter is set too low
T7B02 HRLM (9 - 8)

## Slide 4: What would cause a broadcast AM or FM radio to receive an amateur radio transmission unintentionally?
A. The receiver is unable to reject strong signals outside the AM or FM band
B. The microphone gain of the transmitter is turned up too high
C. The audio amplifier of the transmitter is overloaded
D. The deviation of an FM transmitter is set too low
(A) T7B02 HRLM (9 - 8)

## Slide 5: Which of the following can cause radio frequency interference?
A. Fundamental overload
B. Harmonics
C. Spurious emissions
D. All of these choices are correct
T7B03 HRLM (9 - 8)

## Slide 6: Which of the following can cause radio frequency interference?
A. Fundamental overload
B. Harmonics
C. Spurious emissions
D. All of these choices are correct
(D) T7B03 HRLM (9 - 8)

## Slide 7: Which of the following could you use to cure distorted audio caused by RF current on the shield of a microphone cable?
Band-pass filter
Low-pass filter
Preamplifier
Ferrite choke
T7B04 HRLM (9 - 7)

## Slide 8: Which of the following could you use to cure distorted audio caused by RF current on the shield of a microphone cable?
Band-pass filter
Low-pass filter
Preamplifier
Ferrite choke
(D) T7B04 HRLM (9 - 7)

## Slide 9: How can fundamental overload of a non-amateur radio or TV receiver by an amateur signal be reduced or eliminated?
A. Block the amateur signal with a filter at the antenna input of the affected receiver
B. Block the interfering signal with a filter on the amateur transmitter
C. Switch the transmitter from FM to SSB
D. Switch the transmitter to a narrow-band mode
T7B05 HRLM (9 - 8)

## Slide 10: How can fundamental overload of a non-amateur radio or TV receiver by an amateur signal be reduced or eliminated?
A. Block the amateur signal with a filter at the antenna input of the affected receiver
B. Block the interfering signal with a filter on the amateur transmitter
C. Switch the transmitter from FM to SSB
D. Switch the transmitter to a narrow-band mode
(A) T7B05 HRLM (9 - 8)

## Slide 11: Which of the following actions should you take if a neighbor tells you that your station’s transmissions are interfering with their radio or TV reception?
A. Make sure that your station is functioning properly and that it does not cause interference to your own radio or television when it is tuned to the same channel
B. Immediately turn off your transmitter and contact the nearest FCC office for assistance
C. Install a harmonic doubler on the output of your transmitter and tune it until the interference is eliminated
D. All these choices are correct
T7B06 HRLM (9 - 9)

## Slide 12: Which of the following actions should you take if a neighbor tells you that your station’s transmissions are interfering with their radio or TV reception?
A. Make sure that your station is functioning properly and that it does not cause interference to your own radio or television when it is tuned to the same channel
B. Immediately turn off your transmitter and contact the nearest FCC office for assistance
C. Install a harmonic doubler on the output of your transmitter and tune it until the interference is eliminated
D. All these choices are correct
(A) T7B06 HRLM (9 - 9)

## Slide 13: Which of the following can reduce overload to a VHF transceiver from a nearby FM broadcast station?
A. Installing an RF preamplifier
B. Using double-shielded coaxial cable
C. Installing bypass capacitors on the microphone cable
D. Installing a band-reject filter
T7B07 HRLM (9 - 8)

## Slide 14: Which of the following can reduce overload to a VHF transceiver from a nearby FM broadcast station?
A. Installing an RF preamplifier
B. Using double-shielded coaxial cable
C. Installing bypass capacitors on the microphone cable
D. Installing a band-reject filter
(D) T7B07 HRLM (9 - 8)

## Slide 15: What should you do if something in a neighbor’s home is causing harmful interference to your amateur station?
A. Work with your neighbor to identify the offending device
B. Politely inform your neighbor about the rules that prohibit the use of devices that cause interference
C. Make sure your station meets the standards of good amateur practice
D. All of these choices are correct
T7B08 HRLM (9 - 10)

## Slide 16: What should you do if something in a neighbor’s home is causing harmful interference to your amateur station?
A. Work with your neighbor to identify the offending device
B. Politely inform your neighbor about the rules that prohibit the use of devices that cause interference
C. Make sure your station meets the standards of good amateur practice
D. All of these choices are correct
(D) T7B08 HRLM (9 - 10)

## Slide 17: What should be the first step to resolve non-fiber optic cable TV interference caused by your amateur radio transmission?
Add a low-pass filter to the TV antenna input
Add a high-pass filter to the TV antenna input
Add a preamplifier to the TV antenna input
Be sure all TV feed line coaxial connectors are installed properly
T7B09 HRLM (9 - 10)

## Slide 18: What should be the first step to resolve non-fiber optic cable TV interference caused by your amateur radio transmission?
Add a low-pass filter to the TV antenna input
Add a high-pass filter to the TV antenna input
Add a preamplifier to the TV antenna input
Be sure all TV feed line coaxial connectors are installed properly
(D) T7B09 HRLM (9 - 10)

## Slide 19: What might be a problem if you receive a report that your audio signal through the repeater is distorted or unintelligible?
A. Your transmitter is slightly off frequency
B. Your batteries are running low
C. You are in a bad location
D. All of these choices are correct
T7B10 HRLM (6 - 4)

## Slide 20: What might be a problem if you receive a report that your audio signal through the repeater is distorted or unintelligible?
A. Your transmitter is slightly off frequency
B. Your batteries are running low
C. You are in a bad location
D. All of these choices are correct
(D) T7B10 HRLM (6 - 4)

## Slide 21: What is a symptom of RF feedback in a transmitter or transceiver?
A. Excessive SWR at the antenna connection
B. The transmitter will not stay on the desired frequency
C. Reports of garbled, distorted, or unintelligible voice transmissions
D. Frequent blowing of power supply fuses
T7B11 HRLM (9 - 6)

## Slide 22: What is a symptom of RF feedback in a transmitter or transceiver?
A. Excessive SWR at the antenna connection
B. The transmitter will not stay on the desired frequency
C. Reports of garbled, distorted, or unintelligible voice transmissions
D. Frequent blowing of power supply fuses
(C) T7B11 HRLM (9 - 6)