## Slide 1: Which of the following is good practice when installing ground wires on a tower for lightning protection?
Put a drip loop in the ground connection to prevent water damage to the ground system
Make sure all ground wire bends are right angles
Ensure that connections are short and direct
All these choices are correct
T0B01 HRLM (9 - 5)

## Slide 2: Which of the following is good practice when installing ground wires on a tower for lightning protection?
Put a drip loop in the ground connection to prevent water damage to the ground system
Make sure all ground wire bends are right angles
Ensure that connections are short and direct
All these choices are correct
(C) T0B01 HRLM (9 - 5)

## Slide 3: What is required when climbing an antenna tower?
Have sufficient training on safe tower climbing techniques
Use appropriate tie-off to the tower at all times
Always wear an approved climbing harness
D. All of these choices are correct
T0B02 HRLM (9 - 19)

## Slide 4: What is required when climbing an antenna tower?
Have sufficient training on safe tower climbing techniques
Use appropriate tie-off to the tower at all times
Always wear an approved climbing harness
All of these choices are correct
(C) T0B02 HRLM (9 - 19)

## Slide 5: Under what circumstances is it safe to climb a tower without a helper or observer?
A. When no electrical work is being performed
B. When no mechanical work is being performed
C. When the work being done is not more than 20 feet above the ground
D. Never
T0B03 HRLM (9 - 19)

## Slide 6: Under what circumstances is it safe to climb a tower without a helper or observer?
A. When no electrical work is being performed
B. When no mechanical work is being performed
C. When the work being done is not more than 20 feet above the ground
D. Never
(D) T0B03 HRLM (9 - 19)

## Slide 7: Which of the following is an important safety precaution to observe when putting up an antenna tower?
A. Wear a ground strap connected to your wrist at all times
B. Insulate the base of the tower to avoid lightning strikes
C. Look for and stay clear of any overhead electrical wires
D. All of these choices are correct
T0B04 HRLM (9 - 17)

## Slide 8: Which of the following is an important safety precaution to observe when putting up an antenna tower?
A. Wear a ground strap connected to your wrist at all times
B. Insulate the base of the tower to avoid lightning strikes
C. Look for and stay clear of any overhead electrical wires
D. All of these choices are correct
(C) T0B04 HRLM (9 - 17)

## Slide 9: What is the purpose of a safety wire through a turnbuckle used to tension guy lines?
Secure the guy line if the turnbuckle breaks
Prevent loosening of the turnbuckle from vibration
Provide a ground path for lightning strikes
Provide an ability to measure for proper tensioning
T0B05 HRLM (9 - 17)

## Slide 10: What is the purpose of a safety wire through a turnbuckle used to tension guy lines?
Secure the guy line if the turnbuckle breaks
Prevent loosening of the turnbuckle from vibration
Provide a ground path for lightning strikes
Provide an ability to measure for proper tensioning
(B) T0B05 HRLM (9 - 17)

## Slide 11: What is the minimum safe distance from a power line to allow when installing an antenna?
Add the height of the antenna to the height of the power line and multiply by a factor of 1.5
The height of the power line above ground
1/2 wavelength at the operating frequency
Enough so that if the antenna falls unexpectedly, no part of it can come closer than 10 feet to the power wires
T0B06 HRLM (9 - 17)

## Slide 12: What is the minimum safe distance from a power line to allow when installing an antenna?
Add the height of the antenna to the height of the power line and multiply by a factor of 1.5
B. The height of the power line above ground
C. 1/2 wavelength at the operating frequency
Enough so that if the antenna falls unexpectedly, no part of
can come closer than 10 feet to the power wires
(D) T0B06 HRLM (9 - 17)

## Slide 13: Which of the following is an important safety rule to remember when using a crank-up tower?
A. This type of tower must never be painted
B. This type of tower must never be grounded
C. This type of tower must not be climbed unless retracted or mechanical safety locking devices have been installed
D. All of these choices are correct
T0B07 HRLM (9 - 19)

## Slide 14: Which of the following is an important safety rule to remember when using a crank-up tower?
A. This type of tower must never be painted
B. This type of tower must never be grounded
C. This type of tower must not be climbed unless retracted or mechanical safety locking devices have been installed
D. All of these choices are correct
(C) T0B07 HRLM (9 - 19)

## Slide 15: Which is a proper grounding method for a tower?
A. A single four-foot ground rod, driven into the ground no more than 12 inches from the base
B. A ferrite-core RF choke connected between the tower and ground
C. A connection between the tower base and a cold water pipe
D. Separate eight-foot long ground rods for each tower leg, bonded to the tower and each other
T0B08 HRLM (9 - 17)

## Slide 16: Which is a proper grounding method for a tower?
A. A single four-foot ground rod, driven into the ground no more than 12 inches from the base
B. A ferrite-core RF choke connected between the tower and ground
C. A connection between the tower base and a cold water pipe
D. Separate eight-foot long ground rods for each tower leg, bonded to the tower and each other
(D) T0B08 HRLM (9 - 17)

## Slide 17: Why should you avoid attaching an antenna to a utility pole?
A. The antenna will not work properly because of induced voltages
B. The 60 Hz radiations from the feed line may increase the SWR
C. The antenna could contact high-voltage power lines
D. All of these choices are correct
T0B09 HRLM (9 - 17)

## Slide 18: Why should you avoid attaching an antenna to a utility pole?
A. The antenna will not work properly because of induced voltages
B. The 60 Hz radiations from the feed line may increase the SWR
C. The antenna could contact high-voltage power lines
D. All of these choices are correct
(C) T0B09 HRLM (9 - 17)

## Slide 19: Which of the following is true when installing grounding conductors used for lightning protection?
A. Use only non-insulated wire
B. Wires must be carefully routed with precise right-angle bends
C. Sharp bends must be avoided
D. Common grounds must be avoided
T0B10 HRLM (9 - 5)

## Slide 20: Which of the following is true when installing grounding conductors used for lightning protection?
A. Use only non-insulated wire
B. Wires must be carefully routed with precise right-angle bends
C. Sharp bends must be avoided
D. Common grounds must be avoided
(C) T0B10 HRLM (9 - 5)

## Slide 21: Which of the following establishes grounding requirements for an amateur radio tower or antenna?
A. FCC Part 97 Rules
B. Local electrical codes
C. FAA tower lighting regulations
D. UL recommended practices
T0B11 HRLM (9 - 5)

## Slide 22: Which of the following establishes grounding requirements for an amateur radio tower or antenna?
A. FCC Part 97 Rules
B. Local electrical codes
C. FAA tower lighting regulations
D. UL recommended practices
(B) T0B11 HRLM (9 - 5)